## Slide 1: PYNQ101 – Intro to PYNQ
Presented By: Noah Garcia

## Slide 2: JupyterLab

## Slide 3: Using JupyterLab
JupyterLab is a cell-based GUI (graphical user interface) that allows you to develop and document code incrementally
  It is super helpful for prototyping and developing programs
  We will be using it throughout the bootcamp for PYNQ
The basic components we will be using are:
  Markdown cells
  Code cells
We can interact with the KV260 boards using Python code

## Slide 4: Using Variables
Computers need very specific instructions and that includes telling them when, where, and what we want them to remember.
counter = 0
Memory
counter = counter + 1
Counter: 0
Counter: 1
Index = 2
Index: 2

## Slide 5: Using Lists
Lists are a collection of variables all stored together. They are accessed using an index, which starts at 0.
words = [“monkey”, “dolphin”, “cat”, “lion”]
monkey
words[1] would be “dolphin”
dolphin
cat
lion
words[0]
words[1]
words[2]
words[3]
Memory

## Slide 6: Using If Statements
If statements allow a computer to make decisions based on what is input or what it has in memory.
monkey
dolphin
cat
lion
words[0]
words[1]
words[2]
words[3]
Memory
if words[0] == “monkey”:
print(“True!”)
else:
print(“False ”)
True!

## Slide 7: Using For Loops
For Loops allow us to repeat operations multiple times.
for number in [0, 1, 2, 3]:
print(number)
print("I'm repeating!")
1
I’m repeating!
2
I’m repeating!
3
I’m repeating!
0
I’m repeating!

## Slide 8: Using Libraries
Developers like to share code with each other, and this is done through libraries. They help save time since we can reuse code and develop technology further through collaboration. This is what you will be doing with PYNQ! Some examples of what you can do with a library are shown here:

## Slide 9: Level Up: The FPGA & the DPU
How a Python library can rewire your chip into an AI accelerator

## Slide 10: Where the magic happens: hardware libraries
Our code has been running on the board's CPU — just like a laptop.
But underneath sits re-programmable hardware called an FPGA.
Some libraries (overlays) don't just run code — they rewire the chip.
SOFTWARE library
CPU (the board's regular processor)
changes what your
code DOES
HARDWARE library (overlay)
CPU
runs your
Python
FPGA
does the
heavy work
the overlay adds an FPGA circuit → changes what your chip IS

## Slide 11: What is an FPGA?
FPGA = Field-Programmable Gate Array.
A CPU is like one fast chef doing steps in order.
An FPGA is a box of LEGO for circuits — build many parallel workers.
"Field-programmable" = rebuild it anytime, even inside your board.
CPU = one very fast chef
does steps one after another
Step 1
Step 2
Step 3
one worker, in order
FPGA = box of LEGO circuits
build many workers, all at once
many workers, in parallel

## Slide 12: So what is a DPU?
DPU = Deep-learning Processing Unit — a circuit we build inside the FPGA.
Its job: run neural networks (the brains behind AI) super fast.
It's not a separate chip — it's a design we LOAD with a Python library.
a photo
goes in
DPU inside the FPGA
a factory for AI math
the answer
comes out:
"school bus!"

## Slide 13: Building a DPU in 3 lines of Python
Import the tools, rewire the FPGA, then give it a trained AI model.
The .bit file is the "LEGO instructions"; .xmodel is the AI brain.
Finally grab the runner — your remote control for the DPU.
1
import
DpuOverlay
get the tools
2
DpuOverlay
("dpu.bit")
rewire the FPGA
3
load_model
(".xmodel")
give it an AI brain
▶
overlay
.runner
grab the remote

## Slide 14: The big takeaway
SOFTWARE
changes what your code DOES
HARDWARE
changes what your chip IS
Real AI projects use BOTH: a little Python on the CPU + a DPU doing the heavy lifting in the FPGA